## Slide 1
EE 74099 / EN 74099 Research Project
Members:
ANFM. Begum, GSU. Ahmadh & IIS. Prema Sri
Progress Presentation For The Final Year Project
24.10.2019
Supervised by : Dr. WGCW Kumara & Eng. MFM. Abdul Cader
Project title: Order Management System And Vision Based Autonomous Delivery Robot For Restaurants
Department of Electrical and Telecommunications Engineering
Faculty of Engineering
South Eastern University of Sri Lanka

## Slide 2: Content
Introduction
Objective
Methodology
  Order Management System
  Robot Design and Control
  Image Processing and Path Planning
  External Vision Based Navigation and Path Planning
Appendix

## Slide 3
Our project is mainly on having an external vision based navigation system for indoor robots.
As for the application of it, a restaurant delivery robot will be built and run on this system.
Introduction

## Slide 4
Having a navigation system for internal robots by directing it with an external vision based navigation system and applying the system for restaurant delivery robot
Objective

## Slide 5
In order to achieve this, we are going to deal with our project into three parts as below,
Customer order management system
External vision based path planning
Robot’s hardware and control system
Methodology

## Slide 6
Data Flow Diagram for system

## Slide 7: ORDER MANAGEMENT SYSTEM

## Slide 8
Data Flow Diagram for OMS

## Slide 9
The required webpages were created and the website is now running in the domain fypoms.000webhostapp.com
We have used php, HTML,CSS and JavaScript languages and MariaDB database server for the OMS creation.
Development of the OMS Website

## Slide 10
User Interface

## Slide 11
Admin Interface

## Slide 12: ROBOT DESIGN AND CONTROL

## Slide 13
We did a 3D model for the Robot design we are planning to build.
For the plates we decided to go with Aluminum Composite Material boards because of their strength and light weight.
To connect plates we used threaded rods.
Designing Robot Model

## Slide 14
Bottom plate and L profile – Steel
Bottom plate should have strength to connect
motors and wheels.
Middle and top plates – ACM (Aluminum Composite Material )
The material selected should have strength and
also it should be light weight.
Selection of Material and Components

## Slide 15
NEMA 23 Stepper Motor
TB6600 Stepper Motor Driver
Arduino Uno Microcontroller board
Nvidia Jetson Nano single board computer
Selection of Material and Components

## Slide 16
Building the Robot

## Slide 17
Building the Robot

## Slide 18
Building the Robot

## Slide 19: IMAGE PROCESSING AND PATH PLANNING

## Slide 20
The camera we use should have a wide viewing angle to cover the area.
The images from wide angle cameras has lens distortion. We used camera calibration to remove the effects of lens distortion.
We used MATLAB Camera calibrator from Computer Vision Toolbox.
Before Camera Calibration
Camera Calibration

## Slide 21
Calibration process estimates camera intrinsic, extrinsic, and lens distortion parameters.
Those parameters are used to remove the effects of lens distortion from an image.
After Camera Calibration
Camera Calibration

## Slide 22
We need to pre process image before use it with path planning algorithm. We used MATLAB Computer Vision Toolbox for Image processing.
Image resizing
We used Image resizing to decrease the total number of pixels in the image to reduce the processing power needed and processing time.
Resolution - 3400x4600
Resolution - 360x480
Image Processing

## Slide 23
Image Erosion and dilation
Erosion removes pixels on object boundaries while Dilation adds pixels to the boundaries of objects in an image.
Resized Image
With Image Erosion
With Image Dilation
Image Processing

## Slide 24
Image segmentation
We use Image segmentation to partition the image into multiple segments.
After Image Segmentation
With Image Dilation
Image Processing
Notes: The goal of segmentation is to simplify the representation of an image into something that is more easier to analyze.

## Slide 25
Creating Costmap
Here we creates a 2D Costmap to representing planning space for the path planning algorithm.
After Image Segmentation
Costmap
Path Planning

## Slide 26
Path Planning with RRT algorithm
Creates a path from start point to end point in Costmap using Optimal Rapidly Exploring Random Tree (RRT*) algorithm.
RRT provides a quick solution to generate paths with having no necessity of defining grids and nodes unlike in other shortest path algorithms like Dijkstra.
Planned path in costmap
Path Planning

## Slide 27
Path Planning with RRT algorithm
RRT planner explores the environment from the starting point by constructing a tree of random collision-free poses from start point towards a desired goal region.
For implementation of algorithm, we used MATLAB Robotics toolbox.
Planned path in costmap
Path Planning

## Slide 28
Path Optimization
Later the path is optimized to have minimum nodes with straight paths
Optimized Path
Planned path in Costmap
Path Planning

## Slide 29: EXTERNAL VISION BASED NAVIGATION AND PATH PLANNING
Notes: Thanks Ms Mursina, And good morning everyone. I am Umair Ahmadh, dealing with the part of this project, the navigation system which is the main driving force of our goal. Let me get straight into the show.

## Slide 30: Robot Control and Navigation
Navigation System
Sending Step Counts for each motors to move
Sending current position when obstacle is encountered for path regeneration

## Slide 31: Robot Movement
Camera captures and generate path

## Slide 32: Robot Movement
Robot needs first to rotate towards the next node

## Slide 33: Robot Movement

## Slide 34: Robot Rotation

## Slide 35: Robot Rotation

## Slide 36: Robot Movement

## Slide 37: Piloting the Robot

## Slide 38: Piloting the Robot

## Slide 39: Obstacle Detection
Ultrasonic Sensors detects if any obstacles suddenly come across its path

## Slide 40: Obstacle Detection
If Any obstacles are encountered robot waits for a period and sends to the processing system how many steps it has yet to move from the command it received.
Having it as the current position, navigation system regenerates a new path and pilot the robot according to it.

## Slide 41
2019
2019
Today
Jun
Jul
Aug
Sep
Oct
Nov
Dec
62 days
6/19/2019
8/19/2019
Order Management System
73 days
8/19/2019
10/30/2019
Vision based Obstacle detection and Path Planning
62 days
10/30/2019
12/30/2019
Navigation of the Robot
84 days
6/24/2019
9/15/2019
Building the Robot

## Slide 42
Thank You

## Slide 43: Appendix

## Slide 44
In our design we have 4 wheels and 2 motors.
Here we assume that the coefficient of friction is 0.6 and radius of wheel is 5 cm.
The weight acting on the four wheels can be written as,
N1 is the weight acting on each caster wheel.
N2 on each motor wheel.
The maximum torque is required when the robot starts moving. It should also overcome friction.
To calculate the maximum torque (T),
μ is the coefficient of friction.
N is the average weight acting on each wheel.
r is the radius of wheels.
T is the torque.
Calculation of motor torque

## Slide 45
Assuming that the weight of the robot is equally distributed on all the four wheels,
/ 4
Motor torque required,
m
m
Reference - Learning Robotics using Python by Lentin Joseph
Calculation of motor torque

## Slide 46: Center of Gravity Calculation
P
Based on weight estimation, we did a canter of gravity calculation for the design.
According to the calculation the Center of Gravity of the robot design is 0.235 m above the bottom plate.
It is 9.1cm below the center.

## Slide 47: Center of Gravity Calculation
W1 = 0.8 kg + 1 kg + 0.5 kg
= 2.3 kg x
= 22.54 N
W2 = 0.5 kg + 2.2 kg + 0.4 kg + 0.136 kg + 0.05 kg
= 3.286 kg x
= 32.20 N
W3 = 0.5 kg + 0.2 kg + 1.0 kg
= 1.7 kg
= 16.66 N
W4 = 0.6 kg + 0.15 kg
= 0.75 kg x
= 7.35 N
W5 = 1.2 kg + 0.6 kg
= 1.8 kg x
= 17.64 N
Wtotal = 2.3 kg + 3.286 kg + 1.7 kg + 0.75 kg + 1.8 kg
= 9.836 kg x
= 96.39 N

## Slide 48: Center of Gravity Calculation
Considering the moments around point P in clockwise direction,
W1 x 0 + W2 x 0.3 m + W3 x 0.6 m + W4 x 0.5 m - W5 x 0.04m = Wtotal x X
P
22.54 N x 0 + 32.20 N x 0.3 m + 16.66 N x 0.6 m + 7.35 N x 0.5 m - 17.64 N x 0.04m = 96.39 N x X
9.66 Nm + 9.996 Nm + 3.675 Nm – 0.7 Nm = 96.39 N x X

## Slide 49: Center of Gravity Calculation
=
X = 0.235 m
According to the calculation the Center of Gravity of the robot design is 0.235 m above the bottom plate. It is 9.1cm below the center.

## Slide 50: Calculation of turning angle of the robot
Using the following equation, the angle of rotation of the robot is calculated. Based on which we will rotate the motors to turn the robot to be straight to the next coordinate.
function calculate_Angle(x0,y0,x1,y1){
Robot_rotation_angle
return robot_rotation_angle;
}

## Slide 51: Wheel rotation angle calculation
function motor_steps_for_robot_rotation(robot_rotation_angle){
Left_motor_steps = L * robot_rotation_angle / (3.6*r)
Right_motor_steps = - left_motor_steps
return right_motor_steps, left_motor_steps;
}

## Slide 52: Calculation of straight-line travel distance for the robot
Using the following function, the distance the robot needs to travel in straight in order to reach the next coordinate can be calculated. Based on which we will rotate the motors to drive the robot in straight until reaching the target coordinate.
function calculate_distance(x0, y0, x1, y1){
Calculate robot_straight_travel_distance = ;
return robot_straight_travel_distance;
}

## Slide 53: Calculation of wheel rotations to travel straight to the next coordinate
In one revolution of the wheel, it travels the distance equal to its circumference. Based on this the motor steps can be calculated by using following function.
Function motor_steps_for_robot_travel(robot_straight_travel_distance){
d =robot_straight_travel_distance;
steps = d/(1.8*r);
return right_motor_steps, left_motor_steps;
}