## Slide 1
EE 74099 / EN 74099 Research Project
Members:
ANFM. Begum, GSU. Ahmadh & IIS. Prema Sri
Proposal Presentation For The Final Year Project
12.07.2019
Supervised by : Dr. WGCW Kumara & Eng. MFM. Abdul Cader
Project title: Order Management System And Vision Based Autonomous Delivery Robot For Restaurants
Department of Electrical and Telecommunications Engineering
Faculty of Engineering
South Eastern University of Sri Lanka

## Slide 2: Content
Introduction
Objective
Proposed methodology
  Order Management system
  External vision based navigation and path planning
  Robot design and control
References

## Slide 3
Our project is mainly on having an external vision based navigation system for indoor robots.
As for the application of it, a restaurant delivery robot will be built and run on this system.
3 major sections of the project will be presented
Order Management System
Vision based navigation system
Robot build and control
Introduction

## Slide 4
Customer reserves the table and order food on our system
Management receives order and when it is ready, mark the order as ready to collect
Navigation system gets the starting and destination locations and generating a path based on objects in the environment
Robot follows the path and delivers the food and if it encounters any obstacles, a request made for path regeneration and once the new path is received by the robot it reroutes it’s way along it
And finally, customer takes the food from the robot’s plate
Introduction

## Slide 5: System Diagram
User will put the order through the order management system.
Order will be notified to the chef and chef will place the food on the robot food-placeholder once the order is ready.
Order management system will send a message to the delivery robot to collect the food.
Navigation system will then navigate the robot to the destination table and the customer on the table will take the food.
PDA
Main Server
External camera
User
Chef
PC
Delivery Robot
Figure 1: System diagram

## Slide 6
Having a navigation system for internal robots by directing it with an external vision based navigation system and applying the system for restaurant delivery robot
Objective

## Slide 7
In order to achieve this, we are going to deal with our project into three parts as below,
Customer order management system
External vision based path planning
Robot’s hardware and control system
Proposed methodology

## Slide 8: Order management system

## Slide 9: Order Management System
User interaction can be given via handheld device at the table.
For the purpose for creating web application, we have to deal with a scripting language(PHP), a web server(Apache) and a database(MySQL). Now we are using XAMPP which is combined with X-OS (cross platform), Apache, MySQL and PHP.
Webpage mainly have two interface.
Customer’s interface can be used to ordering the food, table reservation and payment.
Admin’s interface can be used to order updates, food availability and give notification to the robot.

## Slide 10
User can go for ordering page by tapping “Order” menu while admin can login through by tapping “Admin” menu.
Figure 3: Home page

## Slide 11
Admin can update their valid username and password in database. Hence no one can enter the admin page by login. If we enter the correct password server will check the details in database and it will allow to the admin page.
Login page decides who will be going to use the web application.
Figure 4: login window for enter to the administration page

## Slide 12
Admin should be responsible for updating the food availability and the order details in the database. Then it will be shown in customer’s ordering page.
Selected foods by customer can be send through the admin page by getting data from database.
Figure 5: food order list in the user window

## Slide 13
Gantt chart of OMS
Figure 5: Time line

## Slide 14: EXTERNAL VISION BASED NAVIGATION AND PATH PLANNING
Notes: Thanks Ms Mursina, And good morning everyone. I am Umair Ahmadh, dealing with the part of this project, the navigation system which is the main driving force of our goal. Let me get straight into the show.

## Slide 15: Introduction and objectives
A centralized navigation system powered by computer vision
Path planning in an environment with dynamically changing objects
Notes: Where I will be talking about existing systems, how our navigation system is going to be and what we have done so far.

## Slide 16: Existing systems
Fixed path following
  burying an inductive loop or magnets in the floor
  painting lines on the floor
  placing beacons, markers, bar codes etc. in the environment.
Figure 6: Line following robots
Notes: From the literature reviews we have found certain methods of navigation and for positioning of the robots in indoor environments. Summarizing them, leads me to mainly 5 of them. Among which the first is currently in practice for many robots and I will lsit down other possibilities of such systems and the reasone why don’t they stand out in the competition. First one is a simple line following method of navigation, where in the floor there are inductive and magnetic loops buried or recognizable lines drawn on the floor or else there are applications where there are markers on several points of the room to give the robot its location.

## Slide 17
GPS
  For outdoor, the GPS (Global Positioning System) provides a general solution for positioning.
  However, the indoor positioning problem is still open.
Infrared
  its short range
  requiring a line of sight
Notes: And moving on to other possibilities of robot navigation and localization, we have GPS which is a very general solution in the outdoor environment. Howeever in indoor environments a proper solution is having its distance from achieving it.
Moving on to the next solution, Infrared. As its very short range and its requirement of line of sight makes it in the list of not a good option.

## Slide 18
Wi-Max
  range of 50 km
  Too large scope for indoor positioning
Bluetooth
  Detecting Bluetooth signal strength and estimating their movement and location.
  Requires many Bluetooth devices and fluctuates too much
  Thus, it’s not a preferred way.
Notes: The next solutions are WiMax ad Bluetooth. WiMax is having a very long range and thus it makes an suitable selection for an indoor environment. And the Bluetooth as it requires many Bluetooth devices for such a navigation system, it also makes it way harder to be the good solution for this purpose.

## Slide 19: Vision based approach
Lastly, a more advanced way of navigation
Using cameras to navigate the robots
Cameras built in the robot get the surrounding view and objects in front
Notes: Lastly, we have another, a bit advance solution which makes use of computer vision to get the robot navigated to the target position.

## Slide 20: Our approach
Cameras on top of the room gives an overall view of the space
Detection of objects moving around and generating an obstacle map
Based on the current obstacle maps a path is generated from the starting point to the destination
Updating the path dynamically depending on the obstacles on the environment

## Slide 21: Camera Calibration
Figure 5: Camera calibration using chess board
Current progress

## Slide 22
With the use of Homography, we were able to achieve the transformation of camera coordinates to real world coordinates.
Like in the following example,
Source: https://zbigatron.com/mapping-camera-coordinates-to-a-2d-floor-plan/
Transforming camera coordinates
into world coordinates
Figure 5: Transformation of camera coordinates to world coordinates

## Slide 23: Path planning algorithm
As we are dealing with a dynamically changing environment, path planning algorithms like Dijkstra are more likely to be ineffective as they require predefined nodes
Algorithms based on Rapidly exploring random tree (RRT), will be the effective choice for our purpose

## Slide 24: Path planning algorithm
Obstacle map generated with the external cameras will be fed through the algorithm to generate a path
When a sudden object come across the path, sensors on the robot detects and stop the movement. A path regeneration is requested to the system and the robot rerouted with the new path

## Slide 25: Robot Design and Control

## Slide 26: Defining requirements of the robot
The robot should be able to move and supply food to any table avoiding obstacles.
Design should be able to hold electronics components such as microcontrollers, sensors and battery.
The maximum payload robot should be able to carry .
Ground clearance of the robot.
Robot height.
Robot should be of low cost.
To design the body and select components accordingly, first we need to identify the design requirements
One of the easiest designs to satisfy these requirements is TurtleBot, which has a design similar to table design.

## Slide 27: Robot chassis design
It has three layers in the chassis.
The design of our robot will be similar to this with our own moving platform and components.
Moving platform will be designed as a differential drive system.
Source - www.willowgarage.com

## Slide 28: Designing Robot model
We did a 3D model for the Robot design we are planning to build.
For the plates we decided to go with Aluminum Composite Material boards because of their strength and light weight.
To connect plates we will be using threaded rods covered by aluminum tubes.

## Slide 29: Designing Robot model
A rough design of the proposed robot

## Slide 30
The choice of wheel types for a mobile robot is strongly linked to the choice of wheel arrangement, or wheel geometry.
One of the cost-effective solution for mobile robot navigation is differential drive systems[2].
Source : www.semanticscholar.org

## Slide 31: Current progress
Design and weight analysis
Motor torque estimation
Materials and component selection
Building the robot

## Slide 32: Estimation of the robot weight
Item | Weight
ACM Board for 0.378 𝑚2 area | 1.52 𝑘𝑔
Threaded rods for 3.5 m | 2.2 kg
Kinect | 0.6 kg
Aluminum tubes | 0.4 kg
Wheels | 0.6 kg
Power Bank and Battery | 1.0 kg
Motors (NEMA 23) x 2 | 1.2 kg
Other Electronics | 0.5 kg
For foods | 1.0 kg
Steel Bottom plate | 0.8 kg
Total Weight | 9.83 kg

## Slide 33: Estimation Center of Gravity
P
Based on weight estimation, we did a canter of gravity calculation for the design.
According to the calculation the Center of Gravity of the robot design is 0.235 m above the bottom plate.
It is 9.1cm below the center.

## Slide 34: Estimation of required motor torque
In our design we have 4 wheels and 2 motors.
Based on total weight estimation, we did a calculation for required motor torque.
According to the calculations, maximum torque required from a single motor is m.

## Slide 35: Selection of material and components
Bottom plate and L profile – Steel
Bottom plate should have strength to connect
motors and wheels.

## Slide 36: Selection of material and components
Middle and top plates – ACM (Aluminum Composite Material )
The material selected should have strength and
also it should be light weight.

## Slide 37: Selection of material and components
Motor – NEMA 17 Stepper Motor
Holding torque - 1.02 Nm (Required )
Step Angle - 1.8 0
Current - 2A

## Slide 38: Selection of material and components
Motor Driver – TB6600 Stepper Motor Driver
Output Current - up to 4.0A
Micro Step - 1, 2/A, 2/B, 4, 8, 16,32

## Slide 39: Selection of material and components
Microcontroller for driving motor – Arduino Uno
Digital I/O Pins - 14
Operating Voltage - 5V

## Slide 40: Selection of material and components
Main computer - Nvidia Jetson Nano
Quad-core Arm A57 processor @ 1.43 Ghz
4GB System Memory
4 x USB 3.0 ports, 1x USB 2.0 Micro-B port for power

## Slide 41: Building the robot

## Slide 42: Building the robot

## Slide 43: Timeline
Figure 2: Timeline in a Gantt chart

## Slide 44: References
[1] Advanced Science and Technology Letters Vol.112 (Architecture and Civil Engineering 2015), pp.46-49 - Jaegeol Yim
[2] Joseph, L. (2015). Learning Robotics using Python. PACKT.
[3] Siegwart, R., Nourbakhsh, I. R., & Scaramuzza, D. (2011). Introduction to autonomous mobile robots. MIT press.

## Slide 45
Thank You

## Slide 46: Appendix

## Slide 47: Calculation of motor torque
In our design we have 4 wheels and 2 motors.
Here we assume that the coefficient of friction is 0.6 and radius of wheel is 5 cm.
The weight acting on the four wheels can be written as,
N1 is the weight acting on each caster wheel.
N2 on each motor wheel.
The maximum torque is required when the robot starts moving. It should also overcome friction.
To calculate the maximum torque (T),
μ is the coefficient of friction.
N is the average weight acting on each wheel.
r is the radius of wheels.
T is the torque.

## Slide 48: Calculation of motor torque
Assuming that the weight of the robot is equally distributed on all the four wheels,
/ 4
Motor torque required,
m
m
Reference - Learning Robotics using Python by Lentin Joseph

## Slide 49: Center of Gravity Calculation
P
Based on weight estimation, we did a canter of gravity calculation for the design.
According to the calculation the Center of Gravity of the robot design is 0.235 m above the bottom plate.
It is 9.1cm below the center.

## Slide 50
W1 = 0.8 kg + 1 kg + 0.5 kg
= 2.3 kg x
= 22.54 N
W2 = 0.5 kg + 2.2 kg + 0.4 kg + 0.136 kg + 0.05 kg
= 3.286 kg x
= 32.20 N
W3 = 0.5 kg + 0.2 kg + 1.0 kg
= 1.7 kg
= 16.66 N
W4 = 0.6 kg + 0.15 kg
= 0.75 kg x
= 7.35 N
W5 = 1.2 kg + 0.6 kg
= 1.8 kg x
= 17.64 N
Wtotal = 2.3 kg + 3.286 kg + 1.7 kg + 0.75 kg + 1.8 kg
= 9.836 kg x
= 96.39 N

## Slide 51
Considering the moments around point P in clockwise direction,
W1 x 0 + W2 x 0.3 m + W3 x 0.6 m + W4 x 0.5 m - W5 x 0.04m = Wtotal x X
P
22.54 N x 0 + 32.20 N x 0.3 m + 16.66 N x 0.6 m + 7.35 N x 0.5 m - 17.64 N x 0.04m = 96.39 N x X
9.66 Nm + 9.996 Nm + 3.675 Nm – 0.7 Nm = 96.39 N x X

## Slide 52
=
X = 0.235 m
According to the calculation the Center of Gravity of the robot design is 0.235 m above the bottom plate. It is 9.1cm below the center.